# ProLiantDL380G4 - Installing Smart array 6i

Removing Smart Array 6i

The DL380 G4 ships with an integrated Smart Array 6i controller. The benefits include, low-cost, internal and or external channel, and an embedded U320 SCSI Smart Array Controller. The Smart Array 6i has a 64-bit PCI-X, 133MHz system interface, supporting up to 14 devices per channel, with up to 2 TB per logical volume. Additionally it supports:

- 64-bit architecture

- AIT data tapes

- Transportable dual scsi channels

To remove the component:

- Power down the server.

- Extend or remove the server from the rack ("Extending the Server from the Rack", "Removing the Server from the Rack").

- Remove the access panel.

- Remove the PCI riser cage.

- Remove the cable from the plastic retainer.

- Remove the Smart Array 6i cache module.

- Disconnect the cable.

To replace the component, reverse the removal procedure